## Slide 1: Recitation7
李磊
2023/10/25

## Slide 2: Announcements
11/06期中考试, 考到第六章, 大家合理安排复习
下周的回课是期中复习回课
Attacklab 10/26ddl
Archlab 10/31due, 11/02ddl, ddl后会安排同学回顾, 请大家积极报名

## Slide 3: Schedule
张致,宋子青同学回课
助教回顾本周重点内容和相关往年题
讲流水线大题

## Slide 4
Instruction | Fetch | Decode | Execute | Memory r/w | Writeback | PC update
cmovxx | ifun; rA; rB; valP=PC+2 | valA=R[rA] valB=0 | valE=valB+valA cnd=Cond(CC,ifun) |  | if(cnd): R[rB]=valE | PC=valP
irmov | rB; valC; valP=PC+10 |  | valE=0+valC |  | R[rB]=valE | PC=valP
rmmov | rA; rB; valC; valP=PC+10 | valA=R[rA] valB=R[rB] | valE=valB+valC | M8[valE]=valA |  | PC=valP
mrmov | rA; rB; valC; valP=PC+10 | valB=R[rB] | valE=valB+valC | valM=M8[valE] | R[rA]=valM | PC=valP
OP | ifun; rA; rB; valP=PC+2 | valA=R[rA] valB=R[rB] | valE=valA OP valB Set CC |  | R[rB]=valE | PC=valP
jxx | ifun; valC; valP=PC+9 |  | cnd=Cond(CC,ifun) |  |  | PC=cnd? valC : valP
call | valC; valP=PC+9 | valB=R[%rsp] | valE=valB+(-8) | M8[valE]=valP | R[%rsp]=valE | PC=valC
ret |  | valA=R[%rsp] valB=R[%rsp] | valE=valB+8 | valM=M8[valA] | R[%rsp]=valE | PC=valM
push | rA; valP=PC+2 | valA=R[rA] valB=R[%rsp] | valE=valB+(-8) | M8[valE]=valA | R[%rsp]=valE | PC=valP
pop | rA; valP=PC+2 | valA=R[%rsp] valB=R[%rsp] | valE=valB+8 | valM=M8[valA] | R[%rsp]=valE R[rA]=valM | PC=valP

## Slide 5: Points worth noting
Remember what each state does!
Remember the meaning of rA, rB, valA, valB, valC, valE, valM
Note the order of some instruction (think of: push %rsp & pop %rsp)
Use 'cond,' 'cnd,' and 'CC' in the correct format

## Slide 6: Examples (2020)
icode:ifun <- M1[PC]
valP <- PC + 1
valA <- R[%rbp]
valB <- R[%rbp]
valE <- valB + 8
valM <- M8[valA]
R[%rsp] <- ValE
R[%rbp] <- ValM

## Slide 7: Hardware structure
Notice the color of different units
  Blue, gray and white
Five stages
Note the relationship between datapath & control logic
HCL only describes the control logic

## Slide 8: Combinational Circuit & Sequential Circuit
Combinational Circuit
  does not require any sequencing or control
  values propagate through a network of logic gates whenever the inputs change
Sequential Circuit
  controlled via a single clock signal
  Triggered by a clock transition

## Slide 9: Example
Combinational Circuit or Sequential Circuit?
  Register files?
  Data memory?
  ALU?
  CC?
  Instruction memory?
  PC?

## Slide 10: Example
State are updated as clock rises
  CC
  DMEM
  Register file
  PC
The outputs of combinational logic just change as their inputs change
  ALU
  Memory reads

## Slide 11: Make it better?
One clock cycle take too long time;
Most parts of the processor are idle at most time in one cycle;

## Slide 12: Parallelism
Parallelism is one of the greatest ideas in computer architecture.
Parallel threads
Parallel data
Parallel instructions
  More than one instruction at one time

## Slide 13: Law of performance
CPI = Cycles Per Instruction

## Slide 14: Instructions per Program
Determined by
  Algorithm
  Compiler
  ISA

## Slide 15: Clock Cycles per Instruction (CPI)
Determined by
  ISA - Processor implementation
  E.g. for our single-cycle Y86 design, CPI = 1
  For our pipeline Y86 design, CPI > 1
  Superscalar processors, CPI < 1 (we have IPC in this case)

## Slide 16: Time per Cycle
Determined by
  Processor microarchitecture (determines critical path through logic gates)
  Power budget (lower voltages reduce transistor speed)

## Slide 17: Pipeline - philosophy
Need pipeline registers to store the states
Higher throughput
Higher delay

## Slide 18: Problems - Nonuniform Partitioning
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
R
e
g
Clock
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
50 ps
20 ps
150 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Clock
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps

## Slide 19: Problem - Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
  1)Structural hazard
    A required resource is busy(e.g. needed in multiple stages)
    No structural hazard in CSAPP
  2)Data hazard
    Data dependency between instructions
    Need to wait for previous instruction to complete its data read/write
  3)Control hazard
    Flow of execution depends on previous instruction
All hazards can be solved by stalling.

## Slide 20: Solution – data hazard
Forwarding
  Always forward to decode stage
  Note the precedence of data forwarding (e > M > W) (M > E)
cannot resolve load & use sometimes

## Slide 21: Solution – control hazard
For ret, just stall for 3 cycles
  More complex architectures have better methods to avoid stalls caused by 'ret' instructions.
For conditional jump, we can predict whether or not we will take the branch
  Misprediction must be dealt with.

## Slide 22: How can we just stop the pipeline?
By controlling the signals of the pipeline registers!

## Slide 23: How can we just stop the pipeline?
By controlling the signals of the pipeline registers!

## Slide 24: How can we just stop the pipeline?
By controlling the signals of the pipeline registers!

## Slide 25: How to understand the hcl?
HCL describes the logic of gray block in the pipeline.
You can try to combine HCL and the pipeline to understand them better.
Useful tip: try to write your own hcl in your archlab, this will deepen your understanding.
I will give just one example, read the rest by yourself!

## Slide 27: Hazard – control logic
We need a control logic the determine whether there is a hazard.
And if there is, we need some control logics for the pipeline registers to deal with the hazard.
I will also give an example, try out the rest by yourself!

## Slide 29: Combinations:
  ret + misprediction (ret is not executed, and is replaced by a bubble):
    when detected: give F stall and D/E bubble
    cannot both give F stall and give F bubble
  ret + load/use (when the register loaded/used is %rsp; ret is executed):
    when detected: give F/D stall and E bubble

## Slide 30: Exceptions
We store a stat bit in all pipeline registers
Several subtleties
  Multiple exceptions -- the first exception is the most significant
  Mispredicted branch – ignore the exception
If an invalid instruction reaches the memory stage, then the machine is going to stop.
  prevents following instructions from updating CC and other programmer visible states

## Slide 31: Examples
D

## Slide 32: Examples
C

## Slide 33: Examples

## Slide 34: Examples

## Slide 35: Examples
不需要

## Slide 36: Examples
D_icode == IJREGXX: d_valB;
1 2 3

## Slide 37
15 13 20